## Slide 1: Tract-analysis and connectivity
Eleftherios Garyfallidis, PhD
Diffusion Imaging in Python
http://dipy.org
Sherbrooke Connectivity Imaging
Laboratory http://scil.dinf.usherbrooke.ca

## Slide 2: Basic Principles
Streamlines are polylines (a series of line segments) where their points are in floating point coordinates.
These coordinates can be transformed to the image coordinates which are integer coordinates.
An affine transformation is needed to go from streamline coordinates to image coordinates. Given e.g. from the Nifti file.
Interpolation is also needed. Usually trilinear or nearest.
Most common file format is Trackvis (*.trk) or VTK (*.vtk).
Message: Make sure you understand the space of the streamlines in comparison to the space of the images and how to go from the one space to the other. Look at DIPY’s quick start tutorials.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 3: Basic Principles
TODO
  Add figure of bundle and metric map showing the transformation from the one to the other.
  Case 1 streamlines and metrics in the same space.
  Case 2 streamlines and metrics in different space but still having the transformation from the one to the other.
By interpolating the metric values on the points of the streamlines you can address
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 4: Table of contents for tract analysis
Segmentation of streamlines
  Manual
  Automatic
  Semi-automatic
Registration
  Image-based (old school) covered by Konstantinos
  Streamline-based (new) brings many new capabilities
Subject level tractometry
  Statistics of metrics along bundles
  Perpendicular to bundles
Group level tractometry
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 5: Manual segmentation
Types of ROIs:
Inclusion (logical “and” and “or”)
Exclusion (logical “not”)
How we use ROIs:
Termination Points (e.g. Cortical)
Waypoints (e.g. specific white matter region)
Volumetric (e.g. U-Shape)
Available tools:
Trackvis, Fibernavigator and MI-Brain
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 6: Table of contents for connectivity
Cortical surface
  Connect with cortical surface
  Connect with sub-cortical areas
Connectivity
  Understand the basics of graph theory.
  Be critical with counting streamlines.
  An example of good counting with the tractometer.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 7: Table of contents for connectivity
Cortical surface
  Connect with cortical surface
  Connect with sub-cortical areas
Alerts on how to measure connectivity
  Graph theory
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 8: Be critical when counting
Courtesy of Marco Catani
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 9: Be critical when counting
Courtesy of Marco Catani
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 10: Tractometry
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Bells et al. ISMRM 2012, Assaf et al. Neuroimage 2013,
Catani et al, PNAS 2007, Lebel & Beaulieu HBM 2009, Forkel et al Brain 2014
FA1
FA2
FA3
FA4
FA5
FAn-1