## Slide 1: Diffusion Tractography
Eleftherios Garyfallidis, Ph.D.
Diffusion Imaging in Python
http://dipy.org
Sherbrooke Connectivity Imaging
Laboratory (SCIL)
http://scil.dinf.usherbrooke.ca
Notes: Merci Gilles Kahn

## Slide 2: Basic principles

## Slide 3: Main idea: Tensor-based tracking
v1
v2
v3
x
z
λ1
Y.Masutani et al.” European Journal of Radiology 46 (2003)

## Slide 4: Connect the main directions voxel to voxel
v1
v2
v3
x
z
λ1

## Slide 5: Deterministic tracking
If we assume the main eigenvector is tangential to the underlying trajectory of the white matter
Starting from a seed point we can propagate a 3D curve that represents the WM pathway
Two main approaches :
FACT - (Mori et al 1999)
Interpolated Streamlines (Euler, RK, etc) - (Basser et al. 2000)
Streamline Tractography
v1
Seed Point

## Slide 6: Deterministic tracking
E
The track follows a path parallel to the principal eigenvector until the border of the voxel.
  The step size is not fixed
  Works well with low curvature regions
  FACT is used in DTI-Studio and TrackVis
At each step a new direction is interpolated taking into account the surrounding eigenvectors
  Step size is fixed
  Available in Dipy (Garyfallidis, Frontiers 2014)
Step Size
New Position
Old Position
Principal Eigenvector
= + x
FACT Interpolated

## Slide 7: Stopping rules
E
How to stop streamlines ?

## Slide 8: Euler Delta Crossings (EuDX)
E

## Slide 9: Stopping rules
E
How to stop streamlines ?
Level of Anisotropy
Start if FA > threshold and Stop if FA < threshold (FA ~0.15/0.20)
  To avoid regions with low anisotropy (high noise effect and variability)
  To avoid tracking in regions like CSF and GM
Angle of curvature
Fibers should not turn too sharply
Stop if the ANGLE between the old and new direction is > threshold
  it depends on the algorithm used ( e.g FACT vs Euler )
  It depends on the resolution of your dataset ( angle ~30°/ 45°)
θ

## Slide 10
Catani et al. NeuroImage 2002
Lights and Stream-tubes are used to obtain a better 3D visualization.
The size of the tubes is arbitrary and it doesn’t represent the real fascicles!
LONG FIBRES
SHORT FIBRES
Virtual In-Vivo Dissection
Post-Mortem Dissection
The result
Arcuate Fasciculus

## Slide 11
Catani et al. NeuroImage 2002
Lights and Stream-tubes are used to obtain a better 3D visualization.
The size of the tubes is arbitrary and it doesn’t represent the real fascicles!
The result
Cingulum
PARIETAL FIBRES
FRONTAL FIBRES
OCCIPITAL FIBRES
TEMPORAL FIBRES
SHORT FIBRES
LONG FIBRES
Virtual In-Vivo Dissection
Post-Mortem Dissection

## Slide 12
PROJECTION
COMMISSURAL
ASSOCIATION
Corona radiata
Fornix
Corpus callosum
Anterior commissure
Cingulum
Inferior longitudinal
Arcuate
Uncinate
Inferior fronto-occipital
The expectation
Courtesy of Flavio Dell’ Acqua

## Slide 13
Data quality
high SNR
low SNR

## Slide 14
Orientation variability
95% “cone uncertainty”
Courtesy of Derek Jones
Courtesy of Maxime Descoteaux
Measuring variability
Accounting for variability

## Slide 15
Probabilistic Tracking
Low Uncertainty
High Uncertainty
Kaden E et al.Neuroimage, 2007
PICO : Parker GJ, et al. Magn Reson Imaging, vol. 18: 242-54, 2003.
Tractography is repeated multiple times from the same seed to map the intrinsic variability or uncertainty in the data
The results are described a probability/connectivity” maps
The intensity represents the number of streamlines per voxel.
Descoteaux M et al. TMI, 2009

## Slide 16
DTI
HARDI
DTI
HARDI
Multiple orientations

## Slide 17
Thank you
http://scil.dinf.usherbrooke.ca
http://tractometer.org