## Slide 1: Diffusion Tractography
Eleftherios Garyfallidis, Ph.D.
Diffusion Imaging in Python
http://dipy.org
Sherbrooke Connectivity Imaging
Laboratory (SCIL)
http://scil.dinf.usherbrooke.ca
Notes: Merci Gilles Kahn

## Slide 2: Basic principles

## Slide 3: Main idea: Tensor-based tracking
v1
v2
v3
x
z
λ1
Y.Masutani et al.” European Journal of Radiology 46 (2003)

## Slide 4: Connect the main directions voxel to voxel
v1
v2
v3
x
z
λ1

## Slide 5: Deterministic tracking
If we assume the main eigenvector is tangential to the underlying trajectory of the white matter
Starting from a seed point we can propagate a 3D curve that represents the WM pathway
Two main approaches :
FACT - (Mori et al 1999)
Interpolated Streamlines (Euler, RK, etc) - (Basser et al. 2000)
Streamline Tractography
v1
Seed Point

## Slide 6: Deterministic tracking
E
The track follows a path parallel to the principal eigenvector until the border of the voxel.
  The step size is not fixed
  Works well with low curvature regions
  FACT is used in DTI-Studio and TrackVis
At each step a new direction is interpolated taking into account the surrounding eigenvectors
  Step size is fixed
  Available in Dipy (Garyfallidis, Frontiers 2014)
Step Size
New Position
Old Position
Principal Eigenvector
= + x
FACT Interpolated

## Slide 7: Euler Delta Crossings (EuDX)
E

## Slide 8: Euler Delta Crossings (EuDX)
E

## Slide 9: Euler Delta Crossings (EuDX)
E

## Slide 10: Euler Delta Crossings (EuDX)
E

## Slide 11: Euler Delta Crossings (EuDX)
E

## Slide 12: Euler Delta Crossings (EuDX)
E

## Slide 13: Euler Delta Crossings (EuDX)
E

## Slide 14: Stopping rules
E
How to stop streamlines ?

## Slide 15: Stopping rules
E
How to stop streamlines ?
Level of Anisotropy
Start if FA > threshold and Stop if FA < threshold (FA ~0.15/0.20)
  To avoid regions with low anisotropy (high noise effect and variability)
  To avoid tracking in regions like CSF and GM
Angle of curvature
Fibers should not turn too sharply
Stop if the ANGLE between the old and new direction is > threshold
  it depends on the algorithm used (e.g FACT vs Euler)
  It depends on the resolution of your dataset
θ

## Slide 16
Catani et al. NeuroImage 2002
Lights and Stream-tubes are used to obtain a better 3D visualization.
The size of the tubes is arbitrary and it doesn’t represent the real fascicles!
LONG FIBRES
SHORT FIBRES
Virtual In-Vivo Dissection
Post-Mortem Dissection
The result
Arcuate Fasciculus

## Slide 17
Catani et al. NeuroImage 2002
Lights and Stream-tubes are used to obtain a better 3D visualization.
The size of the tubes is arbitrary and it doesn’t represent the real fascicles!
The result
Cingulum
PARIETAL FIBRES
FRONTAL FIBRES
OCCIPITAL FIBRES
TEMPORAL FIBRES
SHORT FIBRES
LONG FIBRES
Virtual In-Vivo Dissection
Post-Mortem Dissection

## Slide 18
PROJECTION
COMMISSURAL
ASSOCIATION
Corona radiata
Fornix
Corpus callosum
Anterior commissure
Cingulum
Inferior longitudinal
Arcuate
Uncinate
Inferior fronto-occipital
The expectation
Courtesy of Flavio Dell’ Acqua

## Slide 19
Data quality
high SNR
low SNR

## Slide 20
Orientation variability
95% “cone uncertainty”
Courtesy of Derek Jones
Courtesy of Maxime Descoteaux
Measuring variability
Accounting for variability

## Slide 21
Probabilistic Tracking
Low Uncertainty
High Uncertainty
Kaden E et al.Neuroimage, 2007
PICO : Parker GJ, et al. MRM, 2003
Tractography is repeated multiple times from the same seed to map the intrinsic variability or uncertainty in the data.
The results are described a probability/connectivity” maps
The intensity represents the number of streamlines per voxel.
Descoteaux M et al. TMI, 2009

## Slide 22
Probabilistic Tracking
Low Reproducibility
High Reproducibility
Deterministic
Probabilistic
Mapping the uncertainty is not mapping the anatomical probability

## Slide 23
Probabilistic Tracking
Noisy datasets will show more 
Uncertainty
Courtesy of Flavio Dell’ Acqua

## Slide 24
Things to remember
Tractography is not always commutative
- Tracking from A to B can be different from tracking from B to A !
Not all software performs tractography in the same way
  Use all the brain as seed-regions and then ROIs are used to visualize only streamlines that pass inside them.
  Others start tracking from a first ROI and then a second ROIs is used to “filter results”.
  Dipy supports both.
  Some software includes Boolean logic rules on tracks and ROIs (AND, OR, NOT) and other operators like CUT or SPLIT to remove “spurious” tracks

## Slide 25
DTI
HARDI
DTI
HARDI
Multiple orientations/crossings

## Slide 26
Multiple orientations/crossings
More fiber orientations to follow…
More changes to get it wrong.
For example, when a large angular threshold is used.

## Slide 27
Applications
of tractography
and some issues

## Slide 28: `
Neurosurgical planning
M. Descoteaux, M. Chamberland and D.Fortin using the Fibernavigator which supports real-time tracking
https://github.com/scilus/fibernavigator
National geographic - February 2014
Neurosurgical planning
Brain tumor

## Slide 29: Automatic tract dissection
Tractography based analysis

## Slide 30: Automatic tract dissection
Garyfallidis et al. Frontiers of Neuroscience 2012

## Slide 31: Tractometry - group studies
Bells et al. ISMRM 2012, Assaf et al. Neuroimage 2013,
Catani et al, PNAS 2007, Lebel & Beaulieu HBM 2009, Forkel et al Brain 2014
FA1
FA2
FA3
FA4
FA5
FAn-1

## Slide 32: Along length statistics
Yeatman PLoS 2010

## Slide 33: Connectomics
Chamberland, Descoteaux et al., HBM 2014

## Slide 34: Rely on counting?
Courtesy of Marco Catani

## Slide 35: Validation
  Wrong connections
  False but plausible connections
  > 50% of streamlines!
www.tractometer.org

## Slide 36
Recent advances
in tractography

## Slide 37: Reducing tractography biases
Masking, seeding, tracking parameters reduce the quantitative strength of comparing bundles of different length, position, width and curvature

## Slide 38: White matter, gray matter, CSF priors for tracking
Girard et al 2012, NeuroImage 2014,, Smith et al. NeuroImage 2012
white matter
gray matter
CSF

## Slide 39: Some results
Without anatomical priors (probabilistic tracking)
Girard et al Descoteaux NeuroImage 2014

## Slide 40: Some results
With anatomical priors (probabilistic tracking)
Girard et al. Descoteaux NeuroImage 2014

## Slide 41: Reducing tractography biases
Better seeding
  reduces the length and curvature bias
Better management of boundaries
  reduces length, volume and density biases
But don’t forget to register well your T1 to the diffusion data

## Slide 42: What next?
  Read the dipy paper [1].
  Read tutorials in dipy.org
  Read the code to understand in detail.
  Run the tracking tutorials.
  Check for evaluation results from the tractometer as they will be coming.
  Literature overview see Garyfallidis and Stamatopoulos PhD theses.
[1] Garyfallidis et al. Frontiers in Neuroinformatics, 2014

## Slide 43
Thank you
http://scil.dinf.usherbrooke.ca
http://tractometer.org