## Slide 1: Tract-analysis and connectivity
Eleftherios Garyfallidis, PhD
Diffusion Imaging in Python
http://dipy.org
Sherbrooke Connectivity Imaging
Laboratory http://scil.dinf.usherbrooke.ca
Research Centre on Aging
http://cdrv.csss-iugs.ca

## Slide 2
Speaker name: Eleftherios Garyfallidis
I have no financial interests or relationships to disclose with regard to the subject matter of this presentation
Declaration of financial interests or relationships

## Slide 3
Connectomics and known issues
2. Tract-analysis and it’s potential
Table of contents
Top-down
Bottom-up

## Slide 4
Structural Connectomics

## Slide 5: Connectomics
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Hagmann et al. PLOS Biology 2008

## Slide 6: Connectivity matrices
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Hagmann et al. PloS Biology 2008
Hagmann et al. PloS Biology 2008

## Slide 7: Can we validate the underlying anatomy?
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Cortical regions may split or merge real bundles
Difficult to check all tract combinations
Alignments with T1 need to be excellent
Cortical regions may vary between subjects
Gong et al. Cereb. Cortex 2009

## Slide 8: Graph theory is powerful
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
As it provides a mathematically sound framework
to study networks.
But it needs good input …
Make sure when you compare different populations that all the preprocessing steps before the matrices are very well done.
Look at the connectomics and then go back and look into the actual bundles. More info next …

## Slide 9: Connectivity analysis (the good guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Valid connections and valid paths
Fiber Cup Phantom
Fillard et al. NeuroImage 2010
Marc-Alex Côté, Neuroimage 2013
Connecting regions of interest (ROIs)

## Slide 10: Connectivity analysis (bad guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Valid connections but wrong path

## Slide 11: Connectivity analysis (more bad guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Invalid connections – connects two regions that shouldn’t be connected

## Slide 12: Connectivity analysis (and the ugly)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Does not connect two end regions – stops prematurely in ventricles or mask

## Slide 13: Alert for connectivity analysis! Be critical when counting streamlines
Courtesy of Marco Catani
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 14: Lesson learned from the ISMRM 2015 tractography challenge: Use the streamlines!
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Voxel perfect alignment with the
T1 is absolutely necessary.
Motion can push your connectivity
results massively.
Counting streamlines going through
ROIs is very sensitive even with a phantom.
Solution! Use model bundles to measure your
connectivity and validate the participants.
Now valid connections are the bundles which are
close to the model bundle up to a distance threshold.
This technique does not require voxel perfect
alignment and can deal with small warps.
But let’s be clear…
Details at tractometer.org

## Slide 15
Tract-analysis

## Slide 16: What is tract-analysis?
By interpolating the metric values on the points of the streamlines we can start talking about bundle integrity and looking into pathology.
The shape of the bundle itself gives also information about the underlying pathology. An example is with the language pathways in autistic populations1.
[1] Lewis et al., Cerebral Cortex, 2013.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
A tract is one of brain’s
superhighways
known from anatomy
A bundle is an
approximation of a tract
using a set of streamlines
Metrics/Maps
FA, AFD, MD etc.
Scalar or Vector.
Tract-analysis is all about bundle-maps.
In this talk I will focus more on the streamlines rather than on the maps.

## Slide 17: Streamlines and images a technical note
Streamlines are 3D curves (a series of line segments) where their points are in floating point coordinates (x=10.3, y=10.5, z=1.8).
This is in contrast to the image coordinates which are integer coordinates (i=10, j=11, k=2).
Common file formats for streamlines are Trackvis (*.trk), VTK, *.tck.
Common file format for metrics is NIfTI (*.nii.gz, *.nii)
More than often a bottleneck in tract-analysis is dealing with the file formats.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Familiarize yourself with the different coordinate systems. See Matthew Brett’s
tutorial on the topic http://nipy.org/nibabel/coordinate_systems.html.
I recommend Nibabel for reading both NIfTI and Trackvis files.
Soon with conversion/correction capabilities for streamline formats.
(x, y, z)
(i, j, k)

## Slide 18: Why streamlines are useful?
  They integrate information along many voxels
  They contain connectivity information (sequential)
  They can tell us about shape and orientation
  Together with other streamlines make “good” models of bundles. Better than using surfaces or just points.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
1
2
20
The order of the points between two
streamlines can be the reverse even in the
same bundle.
1
2
20
20
19
1
To compare streamlines you need to define a distance between streamlines.
Many points… computational expensive and heavy on memory.

## Slide 19: Streamline distances – which one to use ?
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Haussdorff distances1
Computationally expensive
Can put together streamlines of different length.
Streamlines can have different numbers of points
[1] Corouge et al. ISMRM 2004
Vector-like distances2,3
Points are now arrays of
fixed size.
Separate streamlines of
different length.
Very efficient.
[2] Garyfallidis et al. HBM 2010
[3] Guevara et al. HBM 2010

## Slide 20: Streamline distances – which one to use ?
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Minimum Direct Flipped (MDF) distance
Garyfallidis et al., Frontiers 2012
min(ddirect, dflipped)
Fast to compute
Symmetric
Metric distance
Values from 0 to Inf in millimetres
Interpolation along the length is necessary
with fixed number of points. Recommended numbers
are from 12 to 20.
Lower MDF
Higher MDF

## Slide 21: QuickBundles for Simplification
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Using Minimum Direct Flipped (MDF) and
the QuickBundles1 clustering algorithm
This is unsupervised learning. Do not expect to get anatomically relevant clusters as a neuroanatomist would define them. Especially in the case of a whole brain tractography.
For anatomically relevant bundles you need to use supervised learning i.e. have a model of a bundle.
initial
centroids
clusters
[1] Garyfallidis et al., Frontiers 2012
[2] Guevara et al., Neuroimage 2010
[3] O’Donnell et al., IEEE TMI 2008
Very fast
Single distance threshold (mm)
Works with millions of streamlines.
Earlier work on clustering of streamlines2,3.

## Slide 22: Manual segmentation
Types of ROIs:
Inclusion (logical “and” and “or”)
Exclusion (logical “not”)
How we use ROIs:
Termination Points (e.g. Cortical)
Waypoints (e.g. specific white matter region)
Volumetric (e.g. U-Shape)
Available visualization tools:
Trackvis, Fibernavigator and MI-Brain
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Courtesy of Flavio Dell’ Acqua

## Slide 23: Model-based Segmentation
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al., Recognition of bundles in healthy and severely diseased brains, ISMRM 2015.
See also Mayer et al., IEEE TMI 2011
Prasad et al., Neuroimage 2014

## Slide 24: Registration of bundles
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. Robust and efficient linear registration of
fascicles in the space of streamlines, Neuroimage (2015)
The Streamline-based Linear registration (SLR)
is very robust to incomplete data.

## Slide 25: Create bundle-specific atlases using SLR
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al., Neuroimage (2015)
Renauld et al., OHBM (2014)
Atlas of the Optic Radiation
Find overlaps between bundles

## Slide 26: Whole-brain linear registration of streamlines
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. Robust and efficient linear registration of
fascicles in the space of streamlines, Neuroimage (2015)
In brains with large tumors even image-based linear registration can fail. Use this method instead. Register the streamlines not the images.

## Slide 27: Tractometry
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Bells et al. ISMRM 2012, Assaf et al. Neuroimage 2013,
Catani et al, PNAS 2007, Lebel & Beaulieu HBM 2009, Forkel et al Brain 2014
FA1
FA2
FA3
FA4
FA5
FAn-1
Courtesy of Flavio Dell’ Acqua

## Slide 28: Apparent fiber quantification
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Yeatman et al. PLoS 2012
Define planes in MNI space after
registering FA images with nonlinear
registration
Project the planes back in
native space.

## Slide 29: Functional data analysis in tract profiles
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Goodlett et al. Neuroimage 2009
As it is difficult to compare directly
the arc length functions:
The authors used functional data analysis
to fit the profiles as coefficients of
B-splines.
And then used discriminant analysis
with the principal components of
the coefficients of these B-splines.

## Slide 30: Measures along/from a centroid
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Cross-sections along a centroid
Renauld et al., “Morphology of thalamus, LGN and optic radiation do not influence EEG alpha waves”, Brain function and structure (submitted), 2015
Distance maps from centroid

## Slide 31: Comparing sets of streamlines for group comparisons (advanced)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. Frontiers, 2012
Bundle adjacency (BA) is a metric
for comparing how similar are
clusters between different subjects.
The streamlines of all subjects need
to be in the same space.

## Slide 32: Conclusion
  Make the mental leap from images to streamlines. The grid is not everything!
  The world of streamlines is a world of opportunity.
  Automatic segmentation of streamlines is reducing manual segmentation.
  Registration of bundles is robust to incomplete data.
  Clustering/simplification can show you hidden structures and reduce computational complexity.
  Study the bundles using centroids, distances, clusters, cross-sections.
  Do not stick only to Tensor metrics move to AFD, QA and other newer metrics.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 33: Conclusion
  Be critical about how you measure connectivity.
  Make sure you do your pre-processing right.
  Think of more robust ways to measure connectivity and
  use graph theory.
  Combine connectomics with tract-analysis.
  Nearly all the methods shown in this course are available in DIPY (http://dipy.org).
  Find me in the DIPY exhibition booth for more information.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 34: Thank you for your attention!
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)