## Slide 1: Tract-analysis and connectivity
Eleftherios Garyfallidis, PhD
Diffusion Imaging in Python
http://dipy.org
Sherbrooke Connectivity Imaging
Laboratory http://scil.dinf.usherbrooke.ca

## Slide 2: Introduction to tract-analysis
Connecting streamlines to maps
  Streamlines and metrics in the “same” space (native space).
  Streamlines and metrics are in different space but still having the transformation from the one to the other.
By interpolating the metric values on the points of the streamlines we can start talking about bundle integrity
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
A tract is one of brain’s
superhighways
known from anatomy
A bundle is an
approximation of a tract
using a set of streamlines
Metrics/Maps
FA, AFD, MD etc.
Bundle maps

## Slide 3: Streamlines and images
Streamlines are polylines (a series of line segments) where their points are in floating point coordinates (x=10.3, y=10.5, z=1.8).
This is in contrast to the image coordinates which are integer coordinates (i=10, j=11, k=2).
An affine transformation (4x4 transformation matrix) is needed to go from streamline coordinates to image coordinates. Given e.g. from the Nifti file.
Common file formats for streamlines are Trackvis (*.trk), *.vtk, *.tck etc.
Common file formats for metrics is Nifti (*.nii.gz, *.nii)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Warning! Make sure you understand the space of the streamlines in comparison to the
space of the images and how to go from the one space to the other. Familiarize yourself
with RAS 1mm, LAS, LPS etc.
Warning! Know your voxel origin. Is it in the center of the voxel (e.g. Nifti) or in the corner of the voxel (e.g. Trackvis).
(x, y, z)
(i, j, k)

## Slide 4: Why streamlines are useful?
  They integrate information along many voxels
  They contain connectivity information
  They can tell us about shape and orientation
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
1
2
20
Warning! The order of the points between two
streamlines can be the reverse even in the
same bundle.
1
2
20
20
19
1
Warning! These are discrete 3D curves. Difficult to set
coordinate systems along 3D curves. Torsion
and curvature are error prone.
Warning! There is no essence of neighborhood of streamlines
without setting a distance between streamlines.
Warning! Many points… computationally expensive.

## Slide 5: Streamline distances – which one to use ?
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Haussdorff distances
Computationally expensive
Can put together streamlines of different length.
Streamlines can have different numbers of points
Vector-like distances
Points are now arrays of
fixed size.
Separate streamlines
of different length.

## Slide 6: Streamline distances – which one to use ?
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Minimum Direct Flipped (MDF) distance
Garyfallidis et al., Frontiers 2012
min(ddirect, dflipped)
Fast to compute
Symmetric
Metric distance
Values from 0 to Inf in millimetres
Interpolation along the length is necessary
with fixed number of points. Recommended numbers
are from 12 to 20.
Lower MDF
Higher MDF

## Slide 7: QuickBundles for Simplification
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Using Minimum Direct Flipped (MDF) and
the QuickBundles clustering algorithm
Garyfallidis et al., Frontiers 2015
You will be able to identify hidden areas of
your datasets and simplify the computational
load of of processing streamlines.
An easy way to get
Centroids
Clusters
Using a single distance threshold (mm)
Very fast!
Alert! This is unsupervised learning. Do not expect to get anatomically relevant clusters as a neuroanatomist would define them. Especially in the case of a whole brain tractography.
Alert! For anatomically relevant bundles you need to use supervised learning i.e. have a model of the bundles that you are looking for.
initial
centroids
clusters
For other clustering algorithms / distances see the work of Guevara, O’Donnell and Corouge.

## Slide 8: Table of contents for tract analysis
Segmentation of streamlines
  Manual
  Automatic
  Semi-automatic
Registration
  Image-based (old school) covered by Konstantinos
  Streamline-based (new) brings many new capabilities
Subject level tractometry
  Statistics of metrics along bundles
  Perpendicular to bundles
Group level tractometry
  New and exciting
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 9: Manual segmentation
Types of ROIs:
Inclusion (logical “and” and “or”)
Exclusion (logical “not”)
How we use ROIs:
Termination Points (e.g. Cortical)
Waypoints (e.g. specific white matter region)
Volumetric (e.g. U-Shape)
Available tools:
Trackvis, Fibernavigator and MI-Brain
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 10: Automatic Segmentation
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al., Recognition of bundles in healthy and severely diseased brains, ISMRM 2015.

## Slide 11: Registration of bundles
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. Robust and efficient linear registration of
fascicles in the space of streamlines, Neuroimage (2015)
The Streamline-based Linear registration (SLR)
is very robust to incomplete data.

## Slide 12: Create bundle-specific atlases using SLR
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al., Neuroimage (2015)
Atlas of the Optic Radiation
Find overlaps between bundles

## Slide 13: Whole-brain linear registration of streamlines
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. Robust and efficient linear registration of
fascicles in the space of streamlines, Neuroimage (2015)
Tip! In very diseased brains e.g. with large tumors or stroke even image-based linear registration can fail. Use this method instead. Register the streamlines not the images.

## Slide 14: Table of contents for connectivity
Cortical surface
  Connect with cortical surface
  Connect with sub-cortical areas
Connectivity
  Understand the basics of graph theory.
  Be critical with counting streamlines.
  An example of good counting with the tractometer.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 15: Connectivity analysis (the good guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Valid connections and valid paths
Fiber Cup Phantom

## Slide 16: Connectivity analysis (bad guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Valid connections but wrong path

## Slide 17: Connectivity analysis (more bad guys)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Invalid connections – connects two regions that shouldn’t be connected

## Slide 18: Connectivity analysis (and the ugly)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Does not connect two end regions – stops prematurely in ventricles or mask

## Slide 19: Alert for connectivity analysis! Be critical when counting streamlines
Courtesy of Marco Catani
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 20: Lessons from the ISMRM 2015 challenge
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Voxel perfect alignment with the T1 is necessary
Motion can push your connectivity results massively
We need more accurate ways of measuring connectivity
Solution! Use model bundles to measure your connectivity.
Now valid connections are the bundles which are close to the model
bundle up to a distance threshold.
This technique does not require voxel perfect alignment and can
deal with small warps.

## Slide 21: Tractometry
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Bells et al. ISMRM 2012, Assaf et al. Neuroimage 2013,
Catani et al, PNAS 2007, Lebel & Beaulieu HBM 2009, Forkel et al Brain 2014
FA1
FA2
FA3
FA4
FA5
FAn-1

## Slide 22: Apparent fiber quantification
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Yeatman et al. PLoS 2012
Define planes in MNI space after
registering FA images with
nonlinear registration and project
the planes back in native space.

## Slide 23: Functional data analysis
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Goodlett et al. Neuroimage 2009
As it is difficult to compare directly
the arc length functions. The authors
Used functional data analysis to fit the
profiles as coefficients of B-splines.
And then use discriminant analysis
with the principal components of
the coefficients of these B-splines.

## Slide 24: Measures along/from a centroid
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Cross-sections along a centroid
Renauld et al., “Morphology of thalamus, LGN and optic radiation do not influence EEG alpha waves”, Brain function and structure (submitted), 2015
Distance maps from centroid

## Slide 25: Comparing sets of streamlines for group comparisons (advanced)
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)
Garyfallidis et al. PhD thesis,
Univ. of Cambridge, 2012
Bundle adjacency (BA) is a metric
for comparing how similar are
clusters between different subjects.
The streamlines of all subjects need
to be in the same space.

## Slide 26: Conclusion
  Make the mental leap from images to streamlines. The grid is not everything!
  The world of streamlines is a world of opportunity.
  Automatic segmentation of streamlines is reducing manual segmentation.
  Registration of bundles is robust to incomplete data.
  Clustering/simplification can show you hidden structures and reduce computational complexity.
  Study the bundles using centroids, distances, clusters, cross-sections.
  Do not stick only to Tensor metrics move to AFD, QA and other newer metrics.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 27: Conclusion
  Be critical about how you measure connectivity.
  Make sure you do your pre-processing right.
  Nearly all the methods shown in this course are available in DIPY.
  Find me in the DIPY booth for more information.
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)

## Slide 28: Thank you for your attention!
Tract-analysis and connectivity - Eleftherios Garyfallidis (2015)